## Slide 1: LPDNet
CLASS PRESENTATION
A small, fast model to find distracted drivers
Paper: Design and Knowledge Distillation of LPDNet for Efficient Edge Driver Distraction Recognition
Jiazheng Wang · Pyeoungkee Kim
Notes: Hello, everyone. I am Jiazheng Wang. Today I will talk about our paper. Our model is called LPDNet. It is small and fast. It finds distracted drivers.

## Slide 2: The Problem
Many drivers do other things when they drive.
Texting
Phone calls
Drinking
Radio
This is very dangerous.
Goal: a model that is right and fast on a small computer.
Notes: Many drivers do other things when they drive. They use the phone. They drink. They touch the radio. This is very dangerous. A camera in the car can watch the driver. A small computer can tell what the driver is doing. So we need a model that is right and fast.

## Slide 3: Three Hard Points
1 · New drivers
Photos of one driver look alike.
→ Test on new drivers only.
2 · Real speed
A small model can still be slow.
→ Test speed on a Raspberry Pi 5.
3 · Teacher help
A big model teaches a small model. The help changes from model to model.
→ Train with and without the teacher.
Notes: We have three hard points. One: photos of the same driver look alike. So we test on new drivers only. Two: a small model can still be slow. So we test speed on a real small computer, the Raspberry Pi 5. Three: a big model can teach a small model. This help changes from model to model. So we train each model with the teacher and without the teacher. Then we compare.

## Slide 4: Our Model: LPDNet
Built on ShuffleNetV2. A photo goes in on the left. A class comes out on the right.
Idea 1 · direction filters (19 RepDW)
Idea 2 · left-right head
Photo
256×256
Stem
conv
Stage 2
RepDW ×5
Stage 3
RepDW ×9
Stage 4
RepDW ×5
Pool
global
Bilateral
head
Class
1 of 10
Stage 3 features: left half + right half
Notes: Here is the structure of LPDNet. It starts from ShuffleNetV2, a small model. A photo goes in on the left. It passes three stages. In these stages, we change 19 filters. We call them RepDW. This is idea one. The features from stage 3 also go to a new head on the right. This is idea two, the bilateral head. At the end, the model picks one of 10 classes.

## Slide 5: Two New Ideas
In the structure: Idea 1 = the RepDW blocks. Idea 2 = the bilateral head.
Idea 1 · Direction filters
3×3
+
1×5
+
5×1
→
5×5
Training: 3 parts. On the Raspberry Pi: 1 filter.
Each part looks in a different direction.
Idea 2 · Left-right head
Left
Right
Average: Left + Right
Difference: Left − Right
→ Tells the right hand from the left hand.
Notes: Now let me explain the two ideas. Idea one: direction filters. In training, each filter has three parts: 3 by 3, 1 by 5, and 5 by 1. They look in different directions. After training, we merge them into one 5 by 5 filter. Idea two: a left-right head. Some classes use different hands, like texting with the right hand or the left hand. So we cut the features into a left half and a right half. The difference between the halves helps the model tell left from right.

## Slide 6: Teacher and Student
1 · Two views
Normal photo + mirror photo
In the mirror, right becomes left. So the labels switch too.
2 · Learn
Student: LPDNet (small)
Teacher: ConvNeXt-Tiny (big)
The student learns from the true labels and from the teacher.
3 · Use
Remove the teacher.
Only the student runs on the Raspberry Pi 5.
Notes: The teacher is a big model, ConvNeXt-Tiny. The student is our small LPDNet. In training, we use the normal photo and the mirror photo. In the mirror photo, right becomes left, so we switch the labels too. The student learns from the true labels and from the teacher. After training, we remove the teacher. Only the student runs on the Raspberry Pi.

## Slide 7: How We Tested
22,424
photos
26
drivers
10
classes
5 driver groups
Each time, one group is for testing. The test drivers are always new.
Speed test
Raspberry Pi 5 with 4 CPU cores. We count photos per second.
Dataset: State Farm Distracted Driver Detection (Kaggle)
Notes: We use the State Farm dataset. It has about 22 thousand photos from 26 drivers, in 10 classes. We split the drivers into 5 groups. Each time, one group is for testing. So the test drivers are always new. For speed, we count how many photos the Raspberry Pi 5 checks in one second.

## Slide 8: Results
Model | Score (Macro-F1) | Size (million params) | Speed on Pi 5 (photos/s)
Teacher (ConvNeXt-Tiny) | 90.1% | 27.8 | 4.2
LPDNet-X1.5-KD | 88.4% | 2.6 | 60.3
Bilateral-only | 88.2% | 1.3 | 144.9
LPDNet-X1.5-KD compared with the teacher:
−1.7 points
score
11× smaller
size
14× faster
speed
Two choices: higher score (LPDNet-X1.5-KD) or higher speed (Bilateral-only).
Notes: Here are the main results. The teacher scores 90.1 percent, but it checks only 4 photos per second. LPDNet with the teacher scores 88.4 percent. It is only 1.7 points lower. But it is 11 times smaller and 14 times faster. It checks 60 photos per second. Our smaller version, Bilateral-only, scores 88.2 percent and checks 145 photos per second. So we have two choices: a higher score, or a higher speed.

## Slide 9: Does the Teacher Help?
LPDNet-X1.5
87.3%
without teacher
→
88.4%
with teacher
+1.1 points
The score goes up.
ShuffleNetV2-X1.5
87.4%
without teacher
→
86.6%
with teacher
−0.8 points
The score goes down.
The help depends on the student. The changes are small, so we need more tests.
Notes: Does the teacher always help? For LPDNet, yes. The score goes up by 1.1 points. For ShuffleNetV2, the score goes down by 0.8 points. So the teacher's help depends on the student. These changes are small, so we need more tests to be sure.

## Slide 10: Summary
1
LPDNet is small and fast on a Raspberry Pi 5.
2
Two choices: high score or high speed.
3
Teacher help depends on the student.
Next: more datasets, and a live camera in a real car.
Thank you! Questions?
Notes: To sum up. LPDNet is small and fast on a Raspberry Pi 5. It gives two choices: high score or high speed. Teacher help depends on the student. Next, we want to try more datasets and a live camera in a real car. Thank you! Any questions?